Knowledge Probe (Post-Assessment)

|  | Introduction |
| --- | --- |
|  | The purpose of this knowledge probe is to determine your knowledge of MEMS, MEMS applications, fabrication, packaging, and design after viewing the film, MEMS: Making Micro Machines by Ruth Carranza. There are twenty (20) questions. |

- MEMS is an acronym for

  - Micro Energy Manufacturing Systems

  - Microelectromechanical Systems

  - Microelectronics Memory Systems

  - Micro Electron Machines and Semiconductors

  - Many Engineers Making Stuff

- Much of the technology used to fabricate microelectronics (e.g., CMOS chips) can be applied to making MEMS devices.

  - True

  - False

- The MEMS components that move mirrors or other MEMS devices are called ___________.

  - Pressure Sensors

  - Actuators

  - Gyroscopes

  - Accelerometers

  - Yokes

- In a thermal inkjet print head, the heater vaporizes ink to form a __________ that pushes the ink out of the micronozzle.

  - Convection Cycle

  - Mechanical Force

  - Bubble

  - Powder

  - Pixel

- MEMS incorporate microfluidic structures in which of the following applications?

  - Inertial Sensors

  - Digital Mirror Devices

  - Inkjet print heads

  - Blood Pressure Monitors

  - b and c

- Which of the following fluidic properties allows a liquid to refill a microchannel without the use of valves or pumps?

  - Stiction

  - Torsion

  - Energy transfer

  - Capillary action

  - Laminar flow

- The micronozzles in an inkjet print head are so small because

  - the viscosity of the ink requires a smaller channel.

  - more nozzles in a given area allows for greater print resolution (more pixels).

  - turbulence needs to be minimized.

  - small nozzles allow the channels to self-fill with out the need for a mechanical pump.

  - b and d

- The MEMS device used to trigger airbag deployment is a(n)

  - Pressure Sensor

  - Actuator

  - Gyroscope

  - Accelerometer

  - Light Meter

- MEMS are tiny micromachines that can consist of several types of components.  Which of the following types of components would you find in a MEMS?

  - Mechanical

  - Electrical

  - Optical

  - Fluidic

  - All of the above could be found in MEMS

- MEMS inertial sensors sense change in which of the following?

  - Acceleration

  - Pressure

  - Rotation

  - Color

  - a and c

- Digital Mirror Devices are used in which of the following applications?

  - Digital projectors

  - Medical imaging equipment

  - Televisions

  - Data communication networks

  - a and c

- The acronym for the optical MEMS that consists of an array of millions of micromirrors is

  - Digital Mirror Device (DMD)

  - Millions of Mirrors Device (MMD)

  - Digital Pixel Device (DPD)

  - Mirror Array (MA)

  - None of the above

- Which of the following components is used in a MEMS pressure sensor to sense changes in pressure, for example blood pressure or tire pressure?

  - Proof mass

  - Membrane

  - Gyroscope

  - Moveable mirror

  - a and c

- Which of the following MEMS fabrication process steps transfers a pattern onto a light sensitive film on the wafer’s surface?

  - Etch

  - Photolithography

  - Chemical vapor deposition

  - Sputtering

  - Deep Reactive Ion Etch (DRIE)

- Which of the following MEMS fabrication process steps is used to remove unwanted material from a thin film on the surface of the wafer or from within the wafer substrate?

  - Etch

  - Photolithography

  - Chemical vapor deposition

d.   Sputtering

- In MEMS fabrication what is the layer called that provides spacing between two or more moving components by first being deposited and then later removed?

  - Structural layer

  - Conductive layer

  - Sacrificial layer

  - Masking layer

  - Insulating layer

- Which of the following personnel is NOT needed as a member of the design team for a new MEMS device?

  - Mechanical engineer

  - Electrical engineer

  - Marketing personnel

  - Systems engineer

  - All of the above are needed as members of the design team

- Before a MEMS device is sent to manufacturing, a model of the design must be constructed and tested to ensure that the design meets the customer requirements and specifications.

  - True

  - False

  - Most of the time, but not always

- In the game Guitar Hero, accelerometers measure the movement of the guitar by measuring a change in capacitance that is converted to _________ which represents the degree of movement.

  - resistance

  - inductance

  - voltage

  - electromechanical

  - electromagnetic

- Which of the following macro-sized devices is LEAST likely to be redesigned to micro size due to impracticality?

  - A rotary motor

  - Hydraulic pump

  - A gear drive

  - Stadium Lights

  - A syringe