Knowledge Probe (Pre-Assessment)

|  | Introduction |
| --- | --- |
|  | This knowledge probe is part of the learning module based on the film MEMS: Making Micro Machines - An overview of microelectromechanical systems, produced and directed by Ruth Carranza of Silicon Run Production. The purpose of this knowledge probe is to determine your knowledge of MEMS, MEMS applications, fabrication, packaging and design prior to viewing the film. You are not expected to know the answers to the questions. You may be asked to retake an assessment after viewing the film. There are twenty (20) questions. |
|  | MEMS is an acronym for Micro Energy Manufacturing Systems Microelectromechanical Systems Microelectronics Memory Systems Micro Electron Machines and Semiconductors Many Engineers Making Stuff |
|  | MEMS are tiny micromachines that can consist of several types of components. Which of the following types of components would you find in a MEMS? Mechanical Electrical Optical Fluidic All of the above could be found in MEMS |
|  | MEMS inertial sensors sense change in which of the following? Acceleration Pressure Rotation Color a and c |
|  | The MEMS device used to trigger airbag deployment is a(n) Pressure Sensor Actuator Gyroscope Accelerometer Light Meter |

|  | Which of the following components is used in a MEMS pressure sensor to sense changes in pressure, for example blood pressure or tire pressure? Proof mass Membrane Gyroscope Moveable mirror a and c |
| --- | --- |

|  | Digital Mirror Devices are used in which of the following applications? Digital projectors Medical imaging equipment Televisions Data communication networks a and c |
| --- | --- |
|  | MEMS incorporate microfluidic structures in which of the following applications? Inertial Sensors Digital Mirror Devices Inkjet print heads Blood Pressure Monitors b and c |
|  | In a thermal inkjet print head, the heater vaporizes ink to form a __________ that pushes the ink out of the micronozzle. Convection Cycle Mechanical Force Bubble Powder Pixel |
|  | The acronym for the optical MEMS that consists of an array of millions of micromirrors is Digital Mirror Device (DMD) Millions of Mirrors Device (MMD) Digital Pixel Device (DPD) Mirror Array (MA) None of the above |
|  | The MEMS components that move mirrors or other MEMS devices are called ___________. Pressure Sensors Actuators Gyroscopes Accelerometers Yokes |

|  | Which of the following MEMS fabrication process steps transfers a pattern onto a light sensitive film on the wafer’s surface? Etch Photolithography Chemical vapor deposition Sputtering Deep Reactive Ion Etch (DRIE) |
| --- | --- |
|  | Which of the following MEMS fabrication process steps is used to remove unwanted material from a thin film on the surface of the wafer or from within the wafer substrate? Etch Photolithography Chemical vapor deposition Sputtering |

|  | Much of the technology used to fabricate microelectronics (e.g., CMOS chips) can be applied to making MEMS devices. True False |
| --- | --- |
|  | In MEMS fabrication what is the layer called that provides spacing between two or more moving components by first being deposited and then later removed? Structural layer Conductive layer Sacrificial layer Masking layer Insulating layer |
|  | Which of the following fluidic properties allows a liquid to refill a microchannel without the use of valves or pumps? Stiction Torsion Energy transfer Capillary action Laminar flow |
|  | The micronozzles in an inkjet print head are so small because the viscosity of the ink requires a smaller channel. more nozzles in a given area allows for greater print resolution (more pixels). turbulence needs to be minimized. small nozzles allow the channels to self-fill with out the need for a mechanical pump. b and d |

|  | In the game Guitar Hero, accelerometers measure the movement of the guitar by measuring a change in capacitance that is converted to _________ which represents the degree of movement. resistance inductance voltage electromechanical electromagnetic |
| --- | --- |
|  | Which of the following personnel is NOT needed as a member of the design team for a new MEMS device? Mechanical engineer Electrical engineer Marketing personnel Systems engineer All of the above are needed as members of the design team |
|  | Before a MEMS device is sent to manufacturing, a model of the design must be constructed and tested to ensure that the design meets the customer requirements and specifications. True False Most of the time, but not always |
|  | Which of the following macro-sized devices is LEAST likely to be redesigned to micro size due to impracticality? A rotary motor Hydraulic pump A gear drive Stadium Lights A syringe |
| Support for this work was provided by the National Science Foundation's Advanced Technological Education (ATE) Program. |